# Material Safety Data Sheet

SHANGHAI KSTONE INDUSTRIAL CO.,LTD (JIANGSU SUNSHINE INDUSTRY CO.,LTD) OFFICE: 419A,419B ROOM,3B/D,NO.2568,GUDAIROAD,SHANGHAI,CHINA,201100 FACTORY:NO.89, GuGao Road, Taizhou City, Jiangsu China. 225400 www.kstonesurfaces.com freddy@kstonesurfaces.com TEL: +86-13701640271 Prepared By: Mr .Jianbo Yu, Senior Chemist Date: March 21 2019

Basic information of the acrylic artificial stone adhesive

1: 1: Chinese name: plexiglass

2 - methyl - methacrylate homopolymer; polyacrylate plastic; poly (methyl methacrylate); Sol; plexiglass; plexiglass plate

English name:
POLY (METHYL METHACRYLATE)

Synonyms:

METHYL METHACRYLATE POLYMER;METHYL METHACRYLATE, POLYMERIZED;METHYL METHACRYLATE RESIN;METHACRYLIC ACID METHYL ESTER POLYMER;LUCITE;POLY(METHYL METHACRYLATE-CO-ETHYL ACRYLATE);POLY(METHYL METHACRYLATE), ISOTACTIC;POLY(METHYL METHACRYLATE)

CAS No.: 9011-14-7

Molecular formula: C15H24O6X2

Related Categories: Plastic adhesive, esters; polymer materials; Dental Materials; medical polymer; photopolymer; photosensitive functional polymer materials; Polymers,
Mol File: 9011-14-7.mol

2 ACRYFILTER the IR
A single product, a mixture of the difference: a single product (compound)
Composition containing: more than 99% of methyl methacrylate
International Classification Number: without this product
(3) dangerous, hazardous classification category names: the commodity classification benchmark
(4) Police urgent measures:
Enter the eye eye conditions: the plate by cutting the powder into the eyes of the situation, there may be damage to the eye, so do not rub eyes. Use of clean water to wash the foreign body remains in the eye also please accept ophthalmologist diagnosis.
Eat into the situation: through the mouth into the body of its independence is quite low, but, as far as possible, vomiting out if it was abnormal Please accept physician-diagnosed.
5 fire measures:
Fire extinguishing methods: general fire the same way. Combustion will produce harmful methane (methacrylic
methyl) firefighters should be upwind or the use of air cleaners protective masks.
Extinguishing the economy: water, foam fire extinguisher, powder fire extinguishers, and carbon acid gas fire extinguishers.
6. Leakage when the measures: the recycling
Use and safekeeping measures:
Use: 1 Please note that when handling cut hand side plate angle measured.
Plate friction or peel the protective film will generate static electricity are therefore required to prevent static electricity produced by the sound of the disaster.
(3) processing when crushed may fall into the eyes or inhaled so please use the security apparatus.
(4) at room temperature and does not cause fire or combustible materials away from flames.
Storage: Keep away from heat and flames, custody less than a location to store the sunlight.
No leaks, temperature is not high and shall storage.
Exposure prevention measures:
Management concentration: no special set
Device responses: the dust occurs, it is necessary to use the exhaust.
Protective equipment: prevent slippage use protective gloves when handling a large plate.
Avoid dust inhalation use dust masks,
Use protective glasses to prevent dust entering the eye.
Physical / chemical properties:
Appearance: viscous liquid or solid
Specific gravity: 1.19
Melting point: no clear melting point will soften when the temperature area of ​​about 100 ° C above the majority.
Melting degree: does not melt in water
10 The risk of intelligence:
Ignition point: 480 ° C
Flammability: Combustible in contact with the source of fire will burn.
Thermal decomposition: about 300 ° C when heated, will produce methyl methacrylate monomer. This gas will be of low toxicity, irritation of the eyes and respirator may cause dizziness, vomiting, headache and other symptoms.
The outbreak of clearance: None
Security, the reaction: normal temperature and pressure stability.
Harmful to intelligence (human symptoms of patients, including immunology Intelligence):
The living body on school reaction, usually without any harmful.
12 environmental impact information:
No (non-biodegradable)
13 disused Note:
Respect the local legal provisions and manner of burial or incineration.
Incineration, the need to respect the incinerator when the regional law provisions.
Polymethyl methcrylate (PMMA) burning heat value: 2.62 × 104 J / kg
14 transported Note:
The bales inclusions Do damaged.
15 applicable law:
Fire Control Law: Specify flammable synthetic resin (3,000 kg)
Lao law: non-hazardous substances
Toxics Law:
Ship safety law:
Haiphong France:
Other
16 references: None
17 Limitation of Liability (area of ​​responsibility):
The above records to know the information, intelligence and data produced as if new data will be adjusted. The security specifications used in general use for special purposes, the first communication method,
The safe use of the specification does not guarantee.